Incubator for Microplates——DH500

## Introduction:

DH500 Incubator for Microplates which PID fuzzy control technology can accurate to ensure that the temperature control precision and automatically adjust the heating rate, reduce waiting time. It is the ideal automation tool for samples hatching, catalytic reaction process of preserving, blending, save and etc.

Features:

- Easy to set up and use, all information real-time display and showing set

up operation, convenient to observe equipment running status.

- Supports standard microplates and deep well plates.

- Automatic preheating function.

- Automatic power recovery function.

- Temperature calibration function.

- Built-in software and hardware over temperature protection device, will use more reliable.

Applications:

Сytochemistry — for in situ reactions

Immunochemistry — for immunofermentative reactions

Biochemistry — for enzyme and protein analysis

Molecular biology — for micro array analysis

Parameters

| Model | DH500 |
| --- | --- |
| Temp. setting range | 0℃~80℃ |
| Temp control range | RT.+5℃~80℃ |
| Time range | 1min ~ 99h59min/∞ |
| Temp. accuracy | ≤±0.5℃* |
| Display accuracy | 0.1℃ |
| Temp uniformity | ≤±0.5℃* |
| Heating time | ≤10min(from 25℃ to 80℃)* |
| Auto preheating | Yes |
| Auto resume to run | Yes |
| Capacity | 4Microplates or Deepwell plates |
| Power supply | 300W |
| Voltage | AC220V or AC110V/50-60Hz |
| Fuse | 250V 3A Ф5×20 |
| Dimension(mm) | 340x320x200 |
| Weight(kg) | 6.5 |